Upgrading Atlas to feature a camera

Microcontroller chosen: ESP32-S3-WROOM-1-N8R8
Datasheet: https://www.lcsc.com/datasheet/lcsc_datasheet_2411121101_Espressif-Systems-ESP32-S3-WROOM-1-N8R8_C2913201.pdf

XIAO-ESP32S3 Sense:
Link to ebook: https://mjrovai.github.io/XIAO_Big_Power_Small_Board-ebook/

Specification:
Processor: ESP32-S3R8, Xtensa LX7 dual-core, 32-bit processor that operates at up to 240 Mhz
Wireless: Complete 2.4GHz Wi-Fi subsystem; BLE: Bluetooth 5.0, Bluetooth mesh
Built-in Sensors: OV2640 camera sensor for 1600*1200; Digital microphone
Memory: On-chip 8M PSRAM & 8MB Flash; Onboard SD Card Slot, supporting 32GB FAT
Interface: 1x UART, 1x IIC, 1x IIS, 1x SPI, 11x GPIOs (PWM), 9x ADC, 1x User LED, 1x Charge LED, 1x B2B Connector (with 2 additional GPIOs), 1x Reset button, 1x Boot button
Dimentions: 21 x 17.8 x 15mm (with expansion board)
Power:- Input voltage (Type-C): 5V; Input voltage (BAT): 4.2V
- Circuit operating Voltage (ready to operate):
- Type-C: 5V@38.3mA
- BAT: 3.8V@43.2mA (with expansion board)
- Webcam Web application:
- Type-C:
- Average power consumption: 5V/138mA
- Photo moment: 5V/341mA
- Battery:
- Average power consumption: 3.8V/154mA
- Photo moment: 3.8V/304mA
- Microphone recording & SD card writing:
- Type-C:
- Average power consumption: 5V/46.5mA
- Peak power consumption: 5V/89.6mA
- Battery:
- Average power consumption: 3.8V/54.4mA
- Peak power consumption: 3.8V/108mA
- Charging battery current: 100mA

Low Power Consumption Model:
- Without any peripherals:
- Modem-sleep Model: 3.8V/25.5 mA
- Light-sleep Model: 3.8V/2.4 mA
- Deep Sleep Model: 3.8V/63.768 μA
- Connect the camera:
- Modem-sleep Model: 3.8V/44.57 mA
- Light-sleep Model: 3.8V/5.47 mA
- Deep Sleep Model: 3.8V/3.00 mA
- Connecting an SD Card:
- Modem-sleep Model: 3.8V/32.8 mA
- Light-sleep Model: 3.8V/3.48 mA
- Deep Sleep Model: 3.8V/1.08 mA
- Simultaneously connect the camera and the SD card:
- Modem-sleep Model: 3.8V/55.72 mA
- Light-sleep Model: 3.8V/6.56 mA
- Deep Sleep Model: 3.8V/3.98 mA
Wi-Fi Enabled Power Consumptionnn: ~110 mA
BLE Enabled Power Connnnnnnsumptionnnnnnnnnnn: ~102 mA

Pins needed for camera: 14
- 1 XMCLK
- 8 Y#
- 1 PCLK
- 2 I2C (SDA, SCL)
- 1 VSYNC
- 1 HREF
Pins needed f MicroSD: 4	-> Atlas already has MicroSD slot that is counted for
Pins needed for MIC: 2	-> We dont want a mic do ignore.

Schematic and Layout of XIAO-ESP32-S3 Sense​
- [PDF] Seeed Studio XIAO ESP32S3 Sense Schematic
- [Ebook] XIAO: Big Power, Small Board Mastering Arduino and TinyML
- [ZIP] Seeed Studio XIAO ESP32S3 Sense KiCAD Libraries
- [ZIP] Seeed Studio XIAO ESP32S3 Sense Eagle Libraries
- [DXF] Seeed Studio XIAO ESP32S3 Sense Dimension in DXF (top)
- [DXF] Seeed Studio XIAO ESP32S3 Sense Dimension in DXF (bottom)
- [ZIP] Seeed Studio XIAO ESP32S3 Sense Factory firmware
- [XLSX] Seeed Studio XIAO ESP32S3 Sense pinout sheet
- [STEP] Seeed Studio XIAO ESP32S3 Sense 3D Model
- 🔗 [Kicad] Seeed Studio XIAO ESP32S3 Sense FootPrint

And for the bottom layer (XIAO ESP32-S3)​
- [PDF] Seeed Studio XIAO ESP32S3 Schematic
- [ZIP] Seeed Studio XIAO ESP32S3 Eagle Libraries
- [DXF] Seeed Studio XIAO ESP32S3 Dimension in DXF
- [LBR] Seeed Studio XIAO ESP32S3 Eagle footprint
- [ZIP] Seeed Studio XIAO ESP32S3 Factory firmware
- [XLSX] Seeed Studio XIAO ESP32S3 pinout sheet
- [STEP] Seeed Studio XIAO ESP32S3 3D Model
- [ZIP] Seeed Studio XIAO ESP32S3 Certification files
- 🔗 [Kicad] Seeed Studio XIAO ESP32S3 FootPrint

ESP32_CAM_S
Link to schematic: file:///home/sara/Desktop/CameraResearch/esp32_cam_sch.pdf
Pins needed for camera: 14
- 8 Y#	-> 8-bit parallel pixel data
- 1 MCLK	->External clock input from ESP32 to run its internal logic
- 1 PCLK	->Pixel clock. Tells ESP32 when to read the D0–D7 pins
- 2 I2C (SDA, Sck)	-> SDA:Used to configure camera settings (brightness, etc)
-> SCL:Clock line for camera configuration
- 1 VSYNC	->Vertical sync
- 1 HSYNC	->Horizontal reference
Pins needed f MicroSD: 4	-> Atlas already has MicroSD slot that is counted for

[VSYNC] -> Start of Frame
  [HREF] -> Start of Row
    [PCLK] -> New Byte on D0-D7:
      D0-D7: 10010110
      D0-D7: 11000110
    [HREF] Ends -> End of Row
[VSYNC] Ends -> End of Frame

Comparision list
Feature	XIAO ESP32S3	AI-Thinker ESP32-CAM
Chip	ESP32-S3R8 (dual-core LX7)	ESP32 (dual-core LX6)
Flash Memory	8MB	4MB
PSRAM	8MB	4MB
Camera Sensor	OV2640 built-in (on expansion board)	OV2640 built-in
Max Camera Resolution	1600×1200 (UXGA)	1600×1200 (UXGA)
SD Card Slot	Onboard (up to 32GB FAT)	Built-in
Microphone	Digital mic onboard (I2S)	Not included
Battery Support	Contains mountable battery space and recharge	Vin, gnd – no recharge
Wi-Fi	Wi-Fi 4 (802.11 b/g/n)	Wi-Fi 4 (802.11 b/g/n/e/i)
Bluetooth	Bluetooth 5.0 + Mesh	Bluetooth 4.2
USB	Native USB-C (no programmer needed)	Requires external USB-to-Serial adapter
GPIOs (usable)	~11 GPIOs (PWM capable), +2 via B2B connector	9 GPIOs (shared with camera/sd)
Programming & Debugging	Simple: USB-C	Requires external programmer
Camera Interface	Native parallel (LCD_CAM peripheral)	GPIO-based (bit-banged style)
Power Supply	5V via USB-C or 4.2V battery	5V via header
Wi-Fi ON	~110mA	~180mA wif flash OFF
Camera + SD (Photo Moment)	304–341mA peak	310mA with flash ON
Deep Sleep (no peripherals)	63.8 µA	~6mA
Camera + SD (Deep Sleep)	~4mA	Not specified but likely ~6–10mA
Charging Current (USB-C)	100mA	Not built-in

Camera is not available at the lcsc but i found it on alibaba
https://www.alibaba.com/product-detail/Mini-OV2640-2-Million-Pixel-Wide_1601278159929.html?spm=a2700.galleryofferlist.p_offer.d_image.48b413a0DfXOIi&s=p